## Slide 1
Smart Parking System
Parking slot availability and entry control
Team 8
JETHENDRA VARDHAN — 2620030600
LAXMI PRAGYA — 2620030602
VEDA CHANDRA — 2620030606
CHANDRA PAUL — 2620030636
SRIKRISHNA — 2620030675
Project Overview
Uses sensor inputs to check slot availability
Uses Boolean logic to control entry
Shows allow or deny status instantly
DDCA PROJECT
DIGITAL DESIGN
BOOLEAN LOGIC

## Slide 2
The Problem & The Digital Solution
The Problem
Drivers can’t see free slots before entering
Cars still try to enter when full
Manual checks are slow and error-prone
No real-time slot or gate control
The Digital Solution
Turn slot status into binary signals
Use logic gates to read inputs in real time
Detect availability automatically
Allow entry only when available AND requested
Show a live PARKING_FULL signal
Sensor Convention — Binary Input Definitions
Signal | Name | 0 | 1
S1 | Slot 1 | Free | Occupied
S2 | Slot 2 | Free | Occupied
S3 | Slot 3 | Free | Occupied
S4 | Slot 4 | Free | Occupied
E | Entry Request | No | Yes
Key principle: 0 = Free, 1 = Occupied.

## Slide 3
Inputs, Binary States & Parking Conditions
Parking Slot Sensors
S1 — Slot 1
1 = Occupied | 0 = Free
S2 — Slot 2
1 = Occupied | 0 = Free
S3 — Slot 3
1 = Occupied | 0 = Free
S4 — Slot 4
1 = Occupied | 0 = Free
Entry Request
E — Entry Request
1 = Request | 0 = No request
NOT Gate Conversion
Invert each slot signal:
Signal | Meaning | Sn=0 | Sn=1
¬S1 | Slot 1 free | 1 | 0
¬S2 | Slot 2 free | 1 | 0
¬S3 | Slot 3 free | 1 | 0
¬S4 | Slot 4 free | 1 | 0
1 means the slot is free. The OR gate checks overall availability.

## Slide 4
Logic Gates — Sensors to Entry
Stage 1 — NOT
S1 = 1 → ¬S1 = 0
S1 = 0 → ¬S1 = 1
Same for S2, S3, and S4
Stage 2 — OR
Checks if any slot is free:
AVAILABLE = ¬S1 + ¬S2 + ¬S3 + ¬S4
Stage 3 — AND
Entry needs availability and request:
ENTRY_ALLOWED = AVAILABLE · E
= (¬S1 + ¬S2 + ¬S3 + ¬S4) · E
Stage 4 — Full Parking
Parking is full when all slots are occupied:
PARKING_FULL = ¬AVAILABLE = S1 · S2 · S3 · S4
Gate Summary
Gate | Inputs | Output | Use
NOT ×4 | S1–S4 | ¬S1–¬S4 | Invert
OR (4-in) | ¬S1–¬S4 | AVAILABLE | Find free slot
AND (2-in) | AVAIL, E | ENTRY_ALLOWED | Allow entry
NOT (1-in) | AVAILABLE | PARKING_FULL | Full alert
No memory, no clock — just current inputs.

## Slide 5
Logic Gates Connection & Output Flow
Circuit Operation — Left to Right
1
Sensor Inputs
S1–S4 enter as 1 = Occupied, 0 = Free
2
NOT Gates
Invert each sensor: ¬S1, ¬S2, ¬S3, ¬S4
3
OR Gate
AVAILABLE = ¬S1 + ¬S2 + ¬S3 + ¬S4
4
AND Gate + Full Signal
ENTRY_ALLOWED = AVAILABLE · E
PARKING_FULL = ¬AVAILABLE
Worked Examples
Example 1: S1=1, S2=1, S3=0, S4=1, E=1
AVAILABLE = 1
ENTRY_ALLOWED = 1
ENTRY ALLOWED ✓
Example 2: S1=1, S2=1, S3=1, S4=1, E=1
AVAILABLE = 0
PARKING_FULL = 1
ENTRY_ALLOWED = 0
ENTRY DENIED ✗

## Slide 6
Simulation & Decision Logic
Step-by-Step Process
01
Read Sensors
Get S1, S2, S3, S4
02
Invert Signals
Make ¬S1, ¬S2, ¬S3, ¬S4
03
Find Availability
AVAILABLE = ¬S1 + ¬S2 + ¬S3 + ¬S4
04
Check Request
Read input E
05
Decide Entry
ENTRY_ALLOWED = AVAILABLE · E
Simulation Cases
Case A — Spot Free, Entry On
S1=1, S2=0, S3=1, S4=1, E=1
AVAILABLE = 1
ENTRY_ALLOWED = 1
ENTRY PERMITTED ✓
Case B — Parking Full
S1=1, S2=1, S3=1, S4=1, E=1
AVAILABLE = 0
ENTRY_ALLOWED = 0
PARKING_FULL = 1
ENTRY DENIED ✗
Case C — Spot Free, No Entry
S1=1, S2=0, S3=1, S4=1, E=0
AVAILABLE = 1
ENTRY_ALLOWED = 0
NO ENTRY
E must be 1 to allow entry.

## Slide 7
Truth Table & Logic Verification
Simplified Truth Table — Parking Logic
Parking Condition | AVAILABLE | E | ENTRY_ALLOWED | PARKING_FULL
One slot free | 1 | 0 | 0 | 0
One slot free | 1 | 1 | 1 | 0
All slots full | 0 | 0 | 0 | 1
All slots full | 0 | 1 | 0 | 1
ENTRY_ALLOWED = 1 only when AVAILABLE=1 and E=1.
Logic Checks
Free + Request
AVAILABLE=1 and E=1 → ENTRY_ALLOWED=1.
Full Parking
AVAILABLE=0 → ENTRY_ALLOWED=0.
No Request
E=0 → no entry.
No Memory
Output depends only on current inputs.

## Slide 8
Conclusion
Project Summary
4 Binary Sensors
S1–S4 show whether each parking slot is occupied or free.
NOT Gates
Convert occupied slots into free-slot signals: ¬S1, ¬S2, ¬S3, ¬S4.
OR Gate
AVAILABLE = ¬S1 + ¬S2 + ¬S3 + ¬S4
AND Gate
ENTRY_ALLOWED = AVAILABLE · E
Full Parking
PARKING_FULL = S1·S2·S3·S4
Key Design Features
Verified
Matches the truth table.
Scalable
Add more slots by expanding the logic.
Combinational
No clock or memory.
Design Flow
BITS
LOGIC
CIRCUIT
DECISION